## Slide 1
Specialty Devices for Pain Management

## Slide 2
Pulsed RF Advanced Treatment :
Ty Tell

## Slide 3
The Problem:
The Treatment of “neuropathic” chronic pain
Specifically
Multi-level spinal radiculopathies:
Cervical level
Thoracic level
Lumbar level

## Slide 4
Some examples:
Lumbar sciatalgia;
Sciatica referable to L4-L5-S1 roots;
Cervical brachialgia
Postherpetic neuralgia;
Radicular lesions syndroms;
FBSS (Failed Back Surgery Syndrome)

## Slide 5
The solution: Ty Tell
Epidural and trans- ganglion P.R.F. (Pulsed Radio-Frequency) steerable electrocatheter

## Slide 6
Steerability: up to 60°
Distal active tip (electrode), 10 mm.
4F outer diameter, 300 mm length
Infusion from the very end tip of the catheter
Atraumatic
Locking system of the tip
60 ° angle

## Slide 7
Micro- Technology

## Slide 8
Key Features
Because of the steerable tip ( up to 60° angle) the target is easily reached when compared to non-steerable devices
No need to bend the tip by hand
Easier procedure in presence of acute angles (i.e. L5-S1)
Efficient and easy to use in case of multilevel / bilateral treatment
High efficiency of the current flow across the DRG or scar tissue due to the current flow optimization ( dedicated grounding cannula)
Quicker procedure, less Rx exposure
Less traumathic than adesiolysis

## Slide 9
Patient positioning: prone
Surgical approach: - Hiatus Sacralis - Interspinosus
Procedure length: about 30 min.
Success rate measurable within 30 days after the treatment
The treatment can be repeated after
6-8 months in case of relapse

## Slide 10
The catheter is inserted through: - metallic introducer - Seldinger introducer
The catheter is positioned under fluoroscopy
The correct positioning is evaluated by:
  Impedence measurement
  Sensorial Stimulation Test (50Hz)
  Motorial Stimulation Test (2Hz)

## Slide 11
GOALS OF THE OPTIMIZATION CURRENT FLOW
(grounding cannula)
Increase the density of Electric Field on the DRG
To allow the current flow get across the scar tissue (anti-inflammatory effect without adesyolisis)
To reduce the voltage and the time of treatment in PRF, less risk of damages to the nervous tissue

## Slide 12
Catheter Positioning
X Ray Check

## Slide 13
Ty Tell electrode
Cannula with active tip
Ty Tell
Optimization of current flow across the L4-L5 left DRG (a-p view)
Electric field

## Slide 14
Treatment Parameters
Treatment Temp. : 42°C
Treatment Length: 240s (repeated when necessary)
Pulses Length: 20ms
Pulses: 2Hz

## Slide 15
The device is provided with a stylet to allow, when necessary,
a higher level of rigidity